MATERIAL SAFETY DATA SHEET

ANTI-STATIC VIDEO DISPLAY CLEANER				JULY 2000

ANTI-STATIC MULTI-SURFACE CLEANER

STATCLEAN WIPES

STREAKFREE WIPES

LAPTOP/NOTEBOOK WIPES

NON-STREAK WIPES

SECTION I				GENERAL INFORMATION

Distributors name and address:

PerfectData Corporation

110 West Easy Street

Simi Valley, California 93065-1689

(805) 581-4000

EMERGENCY CONTACT:		CHEMTREC (800) 424-9300

PRODUCT:				102495-1	103726-1, 2, 5	104764-1	104765-1

104767-1	104768-1	106046-1

105709-1	105885-1	106037-1	106074-1

106094-1	106142-1	106159-1	106160-1

106225-1	106254-1

NFPA HAZARD RATING

Health (Blue):		1

Flammability (Red):	1

Reactivity (Yellow)	0

_____________________________________________________________________________________________

SECTION II				HAZARDOUS INGREDIENTS

MATERIAL			CAS #		  	TLV (ppm)		%

2- Butoxyethanol    		111-76-2 	    	25 ppm 		2.5%

____________________________________________________________________________________________

SECTION III				PHYSICAL DATA

BOILING POINT (Deg F):	<212			VAPOR PRESSURE (at 68o F):  unknown

APPEARANCE:			Clear  	 		SOLUBILITY IN WATER:	100%

ODOR:				Lavender 		VAPOR DENSITY (Air=1):	unknown

EVAPORATION RATE

(Butyl Acetate = 1):		Slower

MATERIAL SAFETY DATA SHEET

ANTI-STATIC VIDEO DISPLAY CLEANER

ANTI-STATIC MULTI-SURFACE CLEANER 0

STATCLEAN WIPES

STREAKFREE WIPES

LAPTOP/NOTEBOOK WIPES

NON-STREAK WIPES

SECTION IV				FIRE AND EXPLOSION DATA

FLASH POINT (Deg F--Setaflash):  Over 212o F			AUTOIGNITION TEMP (Deg F):	No data

FLAMMABLE LIMITS IN AIR, VOLUME %:	Lower: 	Unknown

Upper:	Unknown

EXTINGUISHING MEDIA:	Water spray, Carbon Dioxide

SPECIAL FIRE FIGHTING

PROCEDURES:		None

UNUSUAL FIRE AND

EXPLOSION HAZARDS:	Keep away from heat, sparks and open flame.

_____________________________________________________________________________________________

SECTION V				HEALTH HAZARD DATA

PRINCIPLE ROUTES

OF EXPOSURE:		Inhalation, skin contact, eyes, ingestion.

CONTACT WITH EYES:	May cause moderate irritation, redness, tearing blurred vision.

CONTACT WITH SKIN:		Prolonged or repeated contact may cause mild irritation.

INHALATION:			Inhalation of vapors may cause dizziness.

INGESTION:			Irritation; may cause vomiting, diarrhea and nausea.

HEALTH EFFECTS OR

RISKS FROM EXPOSURE:	Mild irritation

_____________________________________________________________________________________________

SECTION VI				FIRST AID PROCEDURES

EYES:			Remove contact lenses if worn.  Gently irrigate with large amounts of cool water for 15

minutes.  Do not allow victim to rub eyes.  Seek medical attention if irritation persists.

Do not attempt to neutralize with chemical agents.

SKIN:			Wash affected skin area with soap and water.

INHALATION:		If discomfort is experienced,  remove to fresh air.

INGESTION:		Wash out mouth area and give moderate amounts of fluid (water or milk) to dilute.  Do not 				give anything by mouth if patient is unconscious, very drowsy, or having convulsions.  Do

ANTI-STATIC VIDEO DISPLAY CLEANER

ANTI-STATIC MULTI-SURFACE CLEANER 0

STATCLEAN WIPES

STREAKFREE WIPES

LAPTOP/NOTEBOOK WIPES

NON-STREAK WIPES

SECTION VI (Cont'd)

not give bicarbonate of soda, fruit juices, or vinegar.  If the patient is conscious, induce 				  	vomiting and give fluids again.  Seek medical attention.

SUSPECTED CANCER

AGENT:		None of the components in this material is listed by IARC, NTP, OSHA,

or ACGIH as a carcinogen.

MEDICAL CONDITIONS

AGGRAVATED BY

EXPOSURE:		Pre-existing skin disorders, respiratory diseases and blood diseases.  As with any chemical, 				this product may enhance allergic conditions on certain people.

RECOMMENDATIONS

TO PHYSICIAN:	There is no specific antidote.  Treatment of overexposure should be directed at the control 				of symptoms and the clinical condition.

_____________________________________________________________________________________________

SECTION VII				REACTIVITY DATA

STABILITY:				Stable

CONDITIONS TO AVOID:		Heat , flames, ignition sources

HAZARDOUS DECOMPOSITION:	Not applicable

HAZARDOUS POLYMERIZATION:	Will not occur

_____________________________________________________________________________________________

SECTION VIII				SPILL OR LEAK PROCEDURES

SPILLS:		Mop up or flush to the nearest drain.

WASTE DISPOSAL

METHOD:		Dispose of wastes in accordance with Federal, State and Local regulations.

In the event of an uncontrolled release, the user should determine if the

release is reportable under applicable laws and regulation.

_____________________________________________________________________________________________

ANTI-STATIC VIDEO DISPLAY CLEANER

ANTI-STATIC MULTI-SURFACE CLEANER 0

STATCLEAN WIPES

STREAKFREE WIPES

LAPTOP/NOTEBOOK WIPES

NON-STREAK WIPES

SECTION IX				CONTROL MEASURES

RESPIRATORY

PROTECTION:			Not normally needed.

PROTECTIVE GLOVES:		Not normally needed.

EYE PROTECTION:			Not  normally needed.

OTHER PROTECTIVE

EQUIPMENT:				Not applicable.

OTHER HANDLING

AND STORAGE

REQUIREMENTS:  			Store in original containers in a cool dry area away from other

chemicals and food preparations.

SECTION X				TRANSPORT INFORMATION

PROPER SHIPPING NAME:  		Non-Regulated

HAZARD CLASS:			Non-hazardous	by CFR 49 72.101

UN NUMBER:  				None

This product IS NOT  DOT regulated

_________________________________________________________________________________________________

SECTION XI				SPECIAL PRECAUTIONS

PRECAUTIONARY STATEMENTS:	CAUTION

# KEEP OUT OF REACH OF CHILDREN

Do not get in eyes, on skin or on clothing.  Do not take internally.  Avoid breathing vapors.  If eyes are

contacted, irrigate eyes for 15 minutes.  Seek medical attention if irritation persists.  If skin is contacted, 		  	wash with water.   If discomfort is experienced after prolonged exposure to mists/vapors, remove to fresh

air.  Seek medical attention if discomfort persists.  If ingested, induce vomiting.  Give moderate amounts of 		water or milk.

WORK/HYGIENIC PRACTICES

The recommendations described herein are intended to provide general guidance for minimizing exposure 		and potential risk when handling this product.  Because use conditions will vary depending with each

possible application, specific safe handling procedures should be developed by persons knowledgeable of 		the intended use conditions and equipment.

ANTI-STATIC VIDEO DISPLAY CLEANER

ANTI-STATIC MULTI-SURFACE CLEANER 0

STATCLEAN WIPES

STREAKFREE WIPES

LAPTOP/NOTEBOOK WIPES

## NON-STREAK WIPES

## DISCLAIMER

PERFECTDATA expressly disclaims all express or implied warranties for merchantability and fitness for a particular purpose, with respect to the product or information provided herein.

All information appearing herein is based upon data obtained from the manufacturer and/or recognized technical sources.  While the information is believed to be accurate, PERFECTDATA makes no representations as to its accuracy or sufficiency.  Conditions of use are beyond PERFECTDATA's control and therefore users are responsible to verify this data under their own operation conditions to determine whether the product is suitable for their particular purposes and they assume all risks of their use, handling and disposal of the product, or from the publication, or use of or reliance upon, information contained herein.  This information relates only to the product  designated here and does not relate to its use in combination with any other material or in any other process.