MATERIAL SAFETY DATA SHEET

Complies with OSHA Hazard Communication Standard 29 CFR 1910.1200

Product Type:		Aerosol Cleaner with Ammonia		Emergency Contact: 	Chemtrec

Product Name:		Glass Cleaner 			 		Phone (24 hours):	(800) 424-9300

Part Number(s): 	PD_105843-1					PerfectData Corporation

PO BOX 748

March 2007								NORRISTOWN, PA 19404												GENERAL INFO: 800-973-7332

Section 1 - Identification of Product

COMMON NAME (used on label)(Trade Name & Synonyms):  PerfectData GLASS CLEANER

CAS. NUMBER:  See Section 2

CHEMICAL NAME:  Glycol Ether, Alcohol, & Water

CHEMICAL FAMILY:  N/A

FORMULA:  N/A

### HMIS RATINGS				Minimal Hazard	0

Slight Hazard		1

Health:  	1	 			Moderate Hazard	2

Flammability:	0				Serious Hazard		3

Reactivity:	0				Severe Hazard		4

Personal Protection:  B				Gloves, Safety Glasses	B

Section 2 - Hazardous Ingredients

Principal Hazardous Component(s)

VAPOR

OSHA    AGCIH         PRESSURE                                                                                                                          CHEMICAL AND			                       @ 25 DEG. C.		                      FLASH

COMMON NAME(S)	CAS. #	     PEL         TLV                                           LEL    UEL        POINTDEG. F  % BY WT

Ethyl Alcohol                   64-17-5  1000ppm  1000ppm   44 mmHg                  3.3      19.0          54(TCC)            5 - 10

Ethylene Glycol              (111-76-2)      50ppm        50ppm         0.6mmHg                  1.1         10.6           154 (TCC)             2 - 5

Monobutyl Ether

Liquefied Petroleum Gas  68476-85-7   1000ppm   1000ppm        3691 mmHg            2.0       10.0            -156 Est.                 5 - 10

(Propellant)

Aqua Ammonia             (1336-21-6)     NE              5 mg/m3        n/a                            n/a       n/a               None                     <1

N/A is not available or not applicable

NE is not established

Section 3 - Physical Data

BOILING POINT (Deg. F):  Concentrate Range:  212

SPECIFIC GRAVITY (Water = 1):  Concentrate:  1.0

VAPOR PRESSURE (mmHg):  See Section 2

PERCENT VOLATILE ORGANIC COMPOUNDS:  Less than 10%

VAPOR DENSITY (Air = 1):  >1

EVAPORATION RATE (BA = 1):  >1

SOLUBILITY IN WATER:  Yes

REACTIVITY IN WATER:  None

APPEARANCE AND ODOR:  CONCENTRATE:  Clear liquid, slight ammonia odor;  PROPELLANT:  Colorless, odorless gas; FINISHED PACKAGE:  Pressurized containers.

Section 4 - Fire & Explosion Hazard Data

FLASH POINT:  See Section 2

FLAMMABLE LIMITS IN AIR - % BY VOLUME:  See Section 2

EXTINGUISHER MEDIA:  Water fog, dry chemical, carbon dioxide

AUTO-IGNITION TEMPERATURE:  Unknown

SPECIAL FIRE FIGHTING PROCEDURES:  Water may be used to cool closed containers to prevent pressure build-up and possible bursting when exposed to high temperatures.  Firemen should wear self-contained, positive pressure, respiratory equipment.

UNUSUAL FIRE AND EXPLOSION HAZARDS:  Contents under pressure.  Self-pressurized aerosol containers.  Keep temperature of containers below 120 deg. F. to prevent bursting.

Section 5 - Health Hazard Data

THRESHOLD LIMIT VALUE:  See Section 2

SIGNS AND SYMPTOMS OF EXPOSURE:

EYE CONTACT:  	Contact with liquid or mist may cause irritation, possibly permanent injury.  Vapors may irritate eyes;

SKIN CONTACT:  			Prolonged contact may cause irritation, defatting of skin;  INHALATION: 		 	Overexposure to vapor may cause dizziness, loss of concentration and

irritation.  INTENTIONAL MISUSE BY DELIBERATELY CONCENTRATING AND INHALING THE CONTENTS OF THE CAN MAY BE HARMFUL OR FATAL;

INGESTION:  	Aspiration may cause rapid absorption through the lungs, which may result in systemic effects.

EMERGENCY AND FIRST AID PROCEDURES

INHALATION:  	Remove to fresh air.  If not breathing, give mouth-to-mouth.  If breathing is difficult, give oxygen.   Call a physician.

EYES:  	Flush with water for at least 15 minutes.  Get medical assistance if irritation persists.

SKIN:  	Wash off in flowing water or shower.  Remove contaminated clothing and wash before reuse.

INGESTION:  	Do not induce vomiting.  Call a physician immediately.

Section 6 - Reactivity Data

STABILITY:  Stable

CONDITIONS TO AVOID:  Avoid any excessive heat, ignition sources, open flames, or other high temperatures which induce thermal decomposition.

INCOMPATIBILITY (Materials to Avoid):  None

HAZARDOUS DECOMPOSITION PRODUCTS:  Carbon Dioxide. Carbon MonoxideHAZARDOUS POLYMERIZATION:  Will not occur.

CONDITIONS TO AVOID:  Not Applicable

Section 7 - Spill or Leak Procedures

STEPS TO BE TAKEN IN CASE MATERIAL IS RELEASED OR SPILLED:

SMALL SPILLS:  	Remove ignition sources.  Mop up, wipe up, or soak up immediately.  Use proper protective equipment.

LARGE SPILLS:  	Evacuate area.  Remove ignition sources.  Contain liquid; transfer to closed containers; keep out of water supplies.

WASTE DISPOSAL METHODS:  Dispose in accordance with Federal, State, and Local regulations.  Do not incinerate closed or empty containers.

Section 8 - Special Protection Information

RESPIRATORY PROTECTION:  NIOSH or Bureau of Mines approved organic vapor-type respirator is required in absence of proper environmental control.

VENTILATION:

LOCAL EXHAUST:  To keep below TLV

MECHANICAL (General):  To keep below TLV

SPECIAL:  None

OTHER:  None

PROTECTIVE GLOVES:  Solvent resistant gloves - impervious gloves

EYE PROTECTION:  Safety glasses or goggles

OTHER PROTECTIVE CLOTHING OR EQUIPMENT:  None reasonably foreseeable.

Section 9 – Special Precautions

## PRECAUTIONS TO BE TAKEN

IN HANDLING AND STORAGE: 	Do not store above 110 Deg. F.  Do not use or store near any open flames or ignition sources.

OTHER PRECAUTIONS: 	Contents under pressure.  Do not puncture or incinerate.  Exposure to temperatures above 120 Deg. F may cause can to burst with violence and cause injury.  Vapors are heavier than air and will collect in low areas.

Section 10 - Regulatory Information

SUBJECT TO SECTION 313 OF SARA TITLE III:  Yes Isopropyl Alcohol = 5%

ALL CHEMICAL COMPONENTS ARE LISTED IN THE TSCA INVENTORY.

CHEMICAL LISTED AS CARCINOGEN OR POTENTIAL CARCINOGEN:  NATIONAL TOXICOLOGY PROGRAM:  No

I.A.R.C. MONOGRAPHS:  No

OSHA:  No

OSHA PERMISSIBLE EXPOSURE LIMIT:  See Section 2

AGCIH THRESHOLD LIMIT VALUE:  See Section 2

OTHER EXPOSURE LIMITED USED:  None

Section 11 - Other Information

TRANSPORTATION INFORMATION – DOMESTIC GROUND

Shipping Name:				Consumer Commodity

Hazard Class:				ORM-D

UN Number:				N/A

Packing Group:				N/A

Hazard Label:				None

Carton Marking:			Consumer Commodity, ORM-D

Disclaimer

PERFECTDATA CORPORATION believes that the information contained herein is accurate and reliable as of the date of this material safety data sheet, but no representation guarantee or warranty, express or implied, is made as to the accuracy, reliability, or completeness of the information.  Persons receiving this information are encouraged to make their own determination as to the information’s suitability and completeness for their particular application.  NO INFORMATION CONTAINED HEREIN CONSTITUTES A PRODUCT WARRANTY OF ANY KIND, WHETHER EXPRESS OR IMPLIED; AND ALL IMPLIED WARRANTIES OF MERCHANT ABILITY AND OF FITNESS FOR A PARTICULAR PURPOSE ARE HEREBY DISCLAIMED BY SPRAY PRODUCTS CORPORATION.